## Slide 1
SESSION 2: OUR FIRST PROGRAM
Today's Goal
Write and run our first program
▸ A new webapp: code.gogoboard.org
▸ Learn the Download → Run workflow
Activity 2.2
Time: 30 minutes
Materials: GoGo Board, DC motor, USB cable, computer
Webapp: code.gogoboard.org

## Slide 2
A New Tool
Goodbye pgc.gogoboard.org — hello code.gogoboard.org
▸ In Chapter 1 we recorded programs with the remote
▸ From now on we write programs ourselves
▸ code.gogoboard.org is our main tool from here on
▸ Connection is by USB cable — no WiFi needed
Activity 2.2 — Session 2: Our First Program
2

## Slide 3
Connect to the Webapp (10 min)
1
Open code.gogoboard.org in the browser
2
Connect the GoGo Board with the USB cable
3
Press the connect button, choose "Wired (USB)", select "GoGo Board 7"
4
Find the "Test your board" card and press the bell symbol — hear a beep?
Activity 2.2 — Session 2: Our First Program
3
Notes: Demo on the projector first. If there is no beep, reconnect and select "GoGo Board 7" again. Check that USB cables support data transfer.

## Slide 4
The Program
Motor on 2s → off 1s → on 2s → off → beep
▸ Connect the DC motor to output port 1
▸ Drag the blocks to build this program
▸ Blocks live in the Output, Time, and Sound categories
✎ Workbook — The block table in Activity 2.2 shows which category each block is in
Activity 2.2 — Session 2: Our First Program
4

## Slide 5
Download and Run (15 min)
1
Press Download to send the program to the GoGo Board
2
Press Run — go to the "Run Program" screen on the LCD
3
Watch: the 3 purple LEDs above the LCD light up
4
The motor spins 2s, pauses 1s, spins 2s, then beeps
Activity 2.2 — Session 2: Our First Program
5
Notes: Download only sends the program — nothing happens until Run. This trips up many groups.

## Slide 6
Experiment
Make the program yours
▸ Change the wait times — what happens?
▸ Add more steps
▸ Challenge: can the motor do a short-long-short pattern?
✎ Workbook — Record your experiment in Activity 2.2
Activity 2.2 — Session 2: Our First Program
6

## Slide 7
WHY CODE?
Code gives us precise control over timing and sequence
▸ The LCD menu can turn things on and off
▸ Code says: "on for exactly 2 seconds, then beep"
▸ We decide exactly what happens, and when
Activity 2.2 — Session 2: Our First Program
7

## Slide 8
Reflection
✎ Workbook — Answer the reflection question in Activity 2.2
1. When is using code more useful than controlling through the LCD menu?
Activity 2.2 — Session 2: Our First Program
8